## Slide 1
AIT 500 · WESTCLIFF UNIVERSITY
M.S. ARTIFICIAL INTELLIGENCE
VitalScan
Model Development &
Framework Design
GROUP 1 · rPPG SIGNAL EXTRACTION
WEEK 4 · CLO 2 · CLO 3 · CLO 4
vitalscan.bkre8tive.com
WEEK 4 SUBMISSION
Project: Model Development
and Framework Design
Deliverable 1
Model architecture
Deliverable 2
Chosen algorithms with rationale
Deliverable 3
Data flow diagrams
Reference
Bawack et al. (2021) AI research framework
Germaine Beazer · Jason · Daray · Abner
Notes: Title slide for the Week 4 submission. Three deliverables on the right correspond directly to the assignment brief: (1) model architecture, (2) chosen algorithms with rationale, (3) data flow diagrams. Supplementary reading is Bawack et al. 2021. Submission for AIT 500 / CLO 2 / CLO 3 / CLO 4. Live deployment at vitalscan.bkre8tive.com.

## Slide 2
Assignment context & framework reference
Wk 4 — Project: Model Development and Framework Design · CLO 2 / 3 / 4
AIT 500 · Westcliff University · Group 1 · Week 4 Submission
ASSIGNMENT — verbatim from Moodle
"Begin designing your AI model or framework.
This involves outlining the architecture, defining
algorithms, and determining the data requirements
for your model.
Deliverable: A design document that includes the
model architecture, chosen algorithms, and data
flow diagrams illustrating how your model will function."
CLOs ADDRESSED
• CLO 2 — AI fundamentals: types, methods, and limits
• CLO 3 — Algorithm selection with rationale
• CLO 4 — Applied AI: design + implementation
FRAMEWORK REFERENCE
Bawack et al. (2021)
"A framework for understanding artificial intelligence
research: insights from practice"
J. Enterprise Information Management, 3(2), 645–678
VITALSCAN, MAPPED TO THE FRAMEWORK
• AI capability — computer vision + signal extraction
• Method family — hybrid: pretrained CNN + classical SP
• Application domain — health / contactless biomarkers
• Data type — short facial video (RGB image sequence)
• Validation — supervised held-out on labeled data (UBFC)
• Deployment — production REST API, live containerized stack
Notes: The assignment brief is reproduced verbatim on the left. The right column ties our work to the Bawack et al. (2021) framework — they propose a typology of AI research along several dimensions, and VitalScan maps cleanly to each: we are doing computer-vision-based signal extraction (capability), using a hybrid CNN + classical signal-processing method (method family), applied to health biomarkers (domain), with video as the data type, supervised held-out evaluation, and a live production deployment.

## Slide 3
Problem statement & objective
What the AI model is designed to do, and why
AIT 500 · Westcliff University · Group 1 · Week 4 Submission
INPUT
30-second facial video
• Standard webcam or phone camera · 30 fps
• No special hardware · no contact sensor
• Cooperative subject, mostly frontal, well-lit
OUTPUT
Biomarker JSON contract
• Heart rate (BPM) · HRV SDNN (ms) · stress (0–1)
• Blood pressure placeholder (flagged with low confidence)
• Each biomarker carries {value, confidence, unit}
WHY THIS PROBLEM IS AN AI PROBLEM (CLO 2)
• Perception under noise — pulse signal is 0.1–1 % of reflected light, dominated by lighting and motion artifacts
• Pattern recognition — a learned CNN identifies and tracks the face; classical projection isolates the periodic pulse signature
• Generalization required — the model must work on unseen subjects across skin tone, lighting, and camera variation
• Quantitative output — model produces a continuous heart-rate value with a confidence estimate, not a categorical label
Notes: Problem and objective statement. The input is a 30-second facial video; the output is a biomarker JSON object with four physiological biomarkers, each annotated with a confidence score the downstream consumer can use to weight risk. The lower half explains why this qualifies as an AI problem under CLO 2: perception under heavy noise, pattern recognition through learned and classical methods, generalization to unseen subjects, and quantitative continuous output rather than categorical classification.

## Slide 4
The AI model — architecture
Deliverable 1: hybrid model with pretrained CNN frontend + classical signal-processing backend
AIT 500 · Westcliff University · Group 1 · Week 4 Submission
Architectural choice — hybrid
• Stage 1 — Pretrained deep CNN (MediaPipe FaceMesh, Google) Trained on millions of faces; emits 468 landmarks / frame
• Stage 2 — ROI extraction (polygon mask over forehead + cheeks) Compute mean RGB inside each region per frame
• Stage 3 — POS algorithm (Wang et al. 2017) Linear projection isolates pulse from lighting / motion
• Stage 4 — Butterworth bandpass (0.7–4 Hz, order 3) Zero-phase filter keeps only the heart-rate band
• Stage 5 — FFT + peak in 60–210 BPM band Dominant frequency → heart rate (BPM)
• Stage 6 — Peak detection + IBI → SDNN + LF/HF Same waveform yields HRV and stress index
• Stage 7 — Confidence scoring per biomarker Output: {value, confidence, unit} for each biomarker
Figure 1 — Signal chain (rPPG pipeline)
Notes: Deliverable 1 — model architecture. The model is a HYBRID of one pretrained deep CNN (MediaPipe FaceMesh) followed by six classical signal-processing stages. The CNN stage demonstrates we are using a learned model — it is exactly the kind of multi-layer feature-learning network shown in the cat-classification example from the 2026-05-27 class lecture. The classical stages are explicit, mathematically defined transforms with documented inputs and outputs (defended in our Week 3 research deliverable). Confidence scoring (added 2026-05-25 per professor feedback) ensures every output carries a reliability estimate.

## Slide 5
Chosen algorithms with rationale
Deliverable 2: each stage names the algorithm, its alternatives, and the selection reason
AIT 500 · Westcliff University · Group 1 · Week 4 Submission
Stage
Chosen algorithm
Alternatives considered
Rationale
Face detection
MediaPipe FaceMesh
Haar, dlib HOG, MTCNN, RetinaFace
468 dense landmarks; CPU-realtime; pretrained
ROI extraction
Forehead + cheek polygons
Bounding box, full face, lower face
Highest capillary density; lowest motion
Pulse extraction
POS (Wang 2017)
GREEN, ICA, CHROM, PBV, deep-learning
Strongest classical; interpretable waveform
Bandpass
Butterworth, order 3, filtfilt
Moving average, FIR, Chebyshev
Zero-phase, sharp roll-off, scipy-tested
HR estimation
FFT + peak in 60–210 BPM
Wavelets, autocorrelation, time-domain
Robust on 30-s clips; standard in field
HRV
SDNN (time domain)
RMSSD, pNN50, triangular index
Most widely reported clinical metric
Stress index
LF/HF ratio → sigmoid
Baevsky index, SDNN threshold
Frequency-domain ANS standard
Confidence
Peak prominence + beat count + IBI CV
Bayesian uncertainty, ensemble variance
Math-based, no second model required
Notes: Deliverable 2 — chosen algorithms with rationale. Each row is one pipeline stage: the algorithm selected, the alternatives we considered, and why this one. This table satisfies the assignment's "defining algorithms" requirement. Full reasoning for each row is documented in the Week 3 research deliverable (docs/Week3_Research_AI_Method_Selection.md), which surveys five classical rPPG algorithms and five deep-learning rPPG architectures before justifying POS + MediaPipe as the chosen primary path.

## Slide 6
Data flow diagram — model end-to-end
Deliverable 3: tensor-level data flow with shapes annotated at each stage
AIT 500 · Westcliff University · Group 1 · Week 4 Submission
Video
(900 frames, 1080, 1920, 3)
uint8 RGB · 30 s @ 30 fps
MediaPipe CNN
(900, 468, 3)
pretrained face-mesh landmarks
ROI polygon mask + mean RGB
(900, 3)
mean RGB averaged over forehead + cheeks
POS algorithm (1.6 s window)
(900,)
linear projection isolates pulse signal
Butterworth bandpass 0.7–4 Hz
(900,)
scipy.signal.filtfilt · zero-phase
FFT + peak (60–210 BPM)
scalar BPM
+ confidence from peak-to-mean ratio
Peak detect → IBIs → SDNN, Welch LF/HF
scalar ms · scalar [0,1]
+ confidence from beat-count + IBI plausibility
Biomarker JSON contract
{value, confidence, unit} ×4
shared output to Groups 3 + 4
Blue = ingest/preprocessing · Green = pulse extraction · Amber = biomarker derivation · Red = packaged output
Notes: Deliverable 3 — data flow diagram. Vertical flow shows the exact tensor shape at each stage, what transform produces it, and the implementation detail. Color bands group the stages: ingest + preprocessing in blue, pulse extraction in green, biomarker derivation in amber, packaged output in red. This is the diagram the assignment explicitly asks for — "data flow diagrams illustrating how your model will function."
Key numbers a reviewer can verify: 30 fps × 30 s = 900 frames; MediaPipe outputs 468 landmarks each with (x, y, z); after ROI masking + averaging we collapse to a single (R, G, B) per frame; the entire heavy lifting reduces a 5+ GB raw video down to four scalar biomarkers.

## Slide 7
Data requirements
What the model needs at inference time, and what the ground-truth data must contain to evaluate it
AIT 500 · Westcliff University · Group 1 · Week 4 Submission
INFERENCE INPUT (per scan)
Requirement
Specification
Format
.mp4 / .webm / .mov / .avi / .mkv
Codec
H.264, VP8/9 (extension-permissive)
Duration
30 s preferred (min 5 s)
Frame rate
30 fps (works 24–60)
Resolution
≥360p; face must be detectable
Color
RGB (3 channels)
Subject
1 cooperative face, mostly frontal, lit
Max upload
100 MB
GROUND-TRUTH DATA (per evaluation subject)
Field
Format / range
Video
Same as inference input
PPG waveform
Sampled trace from finger pulse-oximeter
Per-frame HR
BPM, sample-synchronized with video
Timestamps
Seconds, scientific notation
Subject ID
Integer (used for train/test split)
Lighting note
Recorded environment metadata
UBFC schema
video.avi + ground_truth.txt (3 rows)
SCAMPS schema
Simulated PPG (synthetic baseline)
DATASETS — already secured
• UBFC-rPPG — 42 real human subjects · primary benchmark (Univ. de Bourgogne, via Google Drive)
• SCAMPS — 10 synthetic avatar videos · secondary baseline (Microsoft Research, public subset)
Notes: Data requirements split into two halves. Left — what the model needs to run inference on a new video: file format, codec, duration, frame rate, resolution, color, subject conditions, and the 100 MB upload cap. Right — what the ground-truth dataset must contain so we can evaluate model accuracy: the paired video, the PPG waveform, per-frame heart-rate labels, timestamps, and subject identifiers for the train/test split. Both UBFC-rPPG and SCAMPS are already secured and integrated into the evaluation harness.

## Slide 8
Confidence scoring per biomarker
Model-development update — every output carries a {value, confidence, unit} object so downstream consumers can weight by reliability
AIT 500 · Westcliff University · Group 1 · Week 4 Submission
Heart rate
Confidence formula
conf = clip((peak/mean - 1.5) / 4, 0, 1)
What it captures
Ratio of FFT-band peak magnitude to mean magnitude. Sharp dominant peak → high confidence; flat noisy spectrum → low.
HRV (SDNN) + Stress
Confidence formula
conf = min(1, n_peaks/N) × ibi_penalty
What it captures
Beat count vs target N (20 for HRV, 25 for stress). IBI coefficient of variation > 0.30 triggers a penalty for likely missed/extra beats.
Blood pressure
Confidence formula
conf = 0.10 (fixed)
What it captures
Low floor by design. Classical rPPG physically cannot derive BP without per-subject cuff calibration; placeholder value carries a note flag.
WHY THIS MATTERS FOR THE MODEL CONTRACT
• Group 3 (risk classification) weights each biomarker contribution by its confidence — high-confidence reading drives risk more than low
• Low confidence + note field communicates known limits (BP placeholder) without breaking the JSON contract or guessing a value
• Confidence emerges from the math itself (signal SNR, beat count, IBI plausibility) — no second model to train, no additional latency
Notes: Confidence scoring is the model-development update added 2026-05-25 per professor feedback. Each scalar biomarker has a confidence formula derived from signal-quality metrics already computed by the pipeline — no extra model required. Heart-rate confidence is the FFT peak prominence ratio; HRV/stress confidence is beat count modulated by IBI plausibility; BP carries a fixed low confidence with an explanatory note because classical rPPG cannot derive BP. The contract change lets Group 3 weight risk assessments correctly: a high-confidence elevated heart rate should drive the recommendation more strongly than a low-confidence one.

## Slide 9
Validation plan & early results
Held-out evaluation against pulse-oximeter ground truth · classical method has no training step, so the whole UBFC set is held-out
AIT 500 · Westcliff University · Group 1 · Week 4 Submission
VALIDATION STRATEGY
• Primary benchmark — full UBFC-rPPG (n = 42 real subjects)
• Metric 1 — MAE in BPM (primary, rubric target)
• Metric 2 — RMSE in BPM (penalizes outliers)
• Per-subject distribution reported (% within ±1, ±3, ±10)
• Secondary — SCAMPS synthetic-data baseline
• No training step in classical pipeline → whole UBFC = test set
EARLY RESULTS (already measured)
4.06 BPM
MAE on 42 UBFC real-human subjects
Rubric target < 10 BPM · 2.5× headroom
ACCURACY COMPARISON — measured numbers (docs/evaluation_results.md)
Dataset
Algorithm
n
MAE (BPM)
RMSE (BPM)
Verdict
UBFC-rPPG (real)
POS (ours)
42
4.06
7.78
PASS — rubric < 10
UBFC-rPPG (real)
CHROM (baseline)
42
3.86
7.35
PASS — tied
SCAMPS (synthetic)
POS (ours)
10
28.85
38.50
Synthetic-data limit
SCAMPS (synthetic)
CHROM (baseline)
10
34.83
44.05
Worse than POS
Notes: Validation strategy and current measured results. Because the classical pipeline has no learned parameters, there is no training step and the entire 42-subject UBFC dataset functions as the held-out test set. Primary metric is MAE in BPM; secondary is RMSE for outlier sensitivity. Numbers in the bottom table are real measurements from docs/evaluation_results.md.
POS reaches 4.06 BPM MAE on UBFC, clearing the rubric's <10 BPM target by a factor of 2.5. CHROM at 3.86 is statistically tied. On synthetic SCAMPS data the gap widens — POS at 28.85 BPM clearly outperforms CHROM at 34.83 — but synthetic data is a stress test, not the primary benchmark.

## Slide 10
Future model extensions & references
Stretch goals: trained-model artifacts and supporting literature
AIT 500 · Westcliff University · Group 1 · Week 4 Submission
PLANNED MODEL EXTENSIONS
• Level 1 — sklearn regressor over POS-derived features Real train/test split (30/6/6 by subject); ~1 day effort
• Level 2 — 1D CNN on the POS pulse waveform ~3 days; demonstrates end-to-end DL artifact
• Level 3 — PhysNet / TS-CAN from raw frames ~1 week; GPU required; full deep rPPG model
• Level 4 — Blood-pressure regressor on MCD-rPPG Replaces BP placeholder; requires cuff-paired training data
• Bias evaluation — per-skin-tone MAE breakdown on UBFC Honest reporting of demographic performance gaps
REFERENCES
• Bawack, R. E., et al. (2021). A framework for understanding AI research: insights from practice. J. Enterprise Info. Mgmt., 3(2), 645–678.
• Wang, W., den Brinker, A. C., Stuijk, S., de Haan, G. (2017). Algorithmic principles of remote PPG. IEEE TBE 64(7).
• de Haan, G., Jeanne, V. (2013). Robust pulse rate from chrominance-based rPPG. IEEE TBE 60(10).
• Liu, X., et al. (2023). rPPG-Toolbox: deep remote PPG toolbox. NeurIPS Datasets and Benchmarks.
• Bobbia, S., et al. (2019). UBFC-rPPG dataset. Pattern Recog. Letters.
• McDuff, D., et al. (2022). SCAMPS synthetic dataset. Microsoft Research.
• Lugaresi, C., et al. (2019). MediaPipe FaceMesh. arXiv:1906.08172.
• Shaffer, F., Ginsberg, J. P. (2017). HRV metrics and norms. Frontiers in Public Health, 5, 258.
• Group 1 Week 3 deliverable — full method-selection rationale.
Notes: Closing slide — planned model extensions and references. Four levels of extension scoped on the left, from a 1-day sklearn regressor (which directly answers the train/test/eval question) through a 1-week PhysNet / TS-CAN deep-learning model. Bias evaluation is called out separately because the professor flagged demographic performance as a concern on 2026-05-27.
Right column is the reference list. Bawack et al. is the assignment's supplementary reading; the remaining references are the literature underpinning each algorithm choice in the model. Full method-selection rationale lives in our Week 3 deliverable, which functions as the supporting document to this deck.